Flash memory map:

Start	End	Description
00.0000	00.7fff	32 k area for menu system, starts after reset as a module with CBM ID at $8000 (= flash address 0)
00.8000	00.9fff	8 k cartridge disk KERNAL
00.a000	00.afff	4 k settings
00.b000	00.bfff	4 k for flash quick test
00.c000	00.dfff	8 k custom BASIC
00.e000	00.ffff	8 k custom KERNAL
01.0000	03.ffff	3 x 64 k 1st cartridge disk
04.0000	06.ffff	3 x 64 k 2nd cartridge disk
07.0000	0f.ffff	9 x 64 k to store 9 PRG-files
01.0000	1f.ffff	1 mb EasyFlash CRT area, or 16 additional PRG slots

Slot memory map:

$00-$0f: ID to indicate that the slot contains a valid PRG file: ASCII „KERBEROS PRGSLOT“
$10-$2f: ASCIIZ filename (max 31 bytes without the last zero), filled with zeros
$30: control byte
bit 0: 1 = start program in C128 mode, 0 = start in C64 mode
bit 1: 1 = copy BASIC replacement to SRAM before starting the program
bit 2: 1 = copy KERNAL replacement to SRAM before starting the program
$31-$38: unused
$39-$3f: values for registers $de39 - $de3f before starting the program
$40-$41: program load address
$42-$43: program start address (0 = BASIC RUN)
$44-$45: program length
$46-$ff: unused
$100-x : PRG data (without load address), „program length“ number of bytes

SRAM memory map:

$0.0000-$0.9fff: unused
$0.a000-$0.bfff: BASIC replacement
$0.c000-$0.dfff: unused
$0.e000-$0.ffff: KERNAL replacement
$1.0000-$1.ffff: current header and program to start, copied from slot or transfered by MIDI

Transfer:

data transfers encoded in note-off messages:
$8n, n:
bit 3: 1=start of data transfer, 0=data bytes
bit 2: 1=two data bytes, 0=one data byte (second data byte of the note-off message is ignored)
bit 1: bit 7 of first data byte
bit 0: bit 7 of second data byte (if sent)

start of data transfer, with two data bytes ($8c)
first byte: tag ID. If bit 7 is set, then there is no data and the second byte is an optional data byte.
second byte: size-1 (0 means 1 data byte … $ff means $100 data bytes)
last byte in the next data messages: CRC8 checksum (calculated over tag, size and data)

Tags:

see midi_commands.h header file