# C64 MIDI Flash Interface

## Jumpers

JP1: MIDI-thru signal
jumper on 1-2	MIDI-in is routed to MIDI-thru
jumper on 2-3	MIDI-out is duplicated to MIDI-thru

JP2: MC68B50 clock selection
jumper on 1-2	2 MHz
jumper on 2-3	500 kHz

JP3: EXROM
open	flash is disabled
closed	flash is enabled

JP4: MC68B50 interrupt signal routing
jumper on 1-2	NMI
jumper on 2-3	IRQ

## MIDI interface settings
(the menu needs DATEL for filetransfer from PC at the moment)

Emulation	JP2	JP4
Sequential Circuits Inc.	jumper on 2-3	jumper on 2-3
Passport & Syntech	jumper on 2-3	jumper on 2-3
DATEL/Siel/JMS	jumper on 1-2	jumper on 2-3
Namesoft	jumper on 2-3	jumper on 1-2